How to identify the deck clutch from the PTO clutch on MK4 machines

When establishing the difference between the Deck drive clutch, and the PTO drive clutch, there is only one noticeable difference in appearance.  They do however function differently and must only be used for the correct application. You cannot use the PTO clutch to drive the deck or vice versa.

If you look at the three gold studs which are visible on the underside of both clutches, there is an extra hole to the side of one of the gold studs, (indicated above).

The notes below describe how to identify the difference between the two clutches.

DECK DRIVE CLUTCH - This hole is hollow and appears grey or metallic in colour.

PTO DRIVE CLUTCH - This hole has a gold plate behind it and appears gold in colour.

# Text boxes

Part number – 44936100

Part number – 449881100

Gold

Hollow

Deck drive clutch

PTO drive clutch