HOW TO RESET THE SLOPE ALARM

If your slope alarm continuously chirps/bleeps when your Countax/Westwood is turned on then follow the instructions below to reset the slope alarm.

- Park the machine on a level surface

- Turn the machines power off via the key

- locate the tilt sensor (usually found beneath the battery tray)

- Exiting the tilt sensor there should be a green wire that could be cable tied away that is NOT connected to any other wires. In most cases there is a female connector on the end.

- With a donor wire connect this green wire to an earth point (battery negative terminal is fine)

- Whilst the green wire is still connected to the earth turn the machine on but do not start the engine.

- After around 10 seconds you should have heard a quick bleep from the sounder. This indicates that the slope alarm has been reset.

- Turn off the machine

- Remove the donor wire from the green wire terminal and the earthing point.

- Turn the machine back on and test machine and slope alarm

If the sounder continues to chirp/bleep then there is likely to be terminal damage to the tilt sensor itself and this may need to be replaced.